## Slide 1: ERU High-Level Processing – Object Detection
Hardware/Software tools utilized
  Raspberry Pi 4, HD USB webcam (CV2), Google coral edge TPU
  Ubuntu 20.04, Google Colab, TFLite, LabelIMG, Python3.8
  PiicoDev Laser Distance Sensor
Network
  Efficientdet_lite_0(current), possibly 0~2 can be used.
  Originally trained on COCO(Common Objects in Context) 2017 dataset, optimized for TFLite, designed for performance on mobile CPU, GPU, and EdgeTPU.
  Retrained through Google Colab using custom dataset (hiker, package, cone, and box).
Implementation
  Upon detecting obstacle, I/O signal is sent from inference python script
  FPS(Frames per second) and Distance (in mm) printed on live camera screen
  Signals will be packaged and interpreted via ROS

## Slide 2: ERU High-Level Processing – Object Detection

## Slide 3: ERU High-Level Processing – Object Detection
Wireless Video Transmission using NDI
  FPS measured: About 15~17, max 20
NDI Protocol Specifications
  By default, it transmits using UDP
  Many endpoints can watch the video source on the network
  Utilizes mDNS (multicast Domain Name System) to allow for zero configuration discovery
Demo video Link:
https://youtu.be/-JaYwJnfG48